## Slide 1: Theory and implementation of optimisation methods for optimizations in distribution power system – PART 1
Marinko Barukčić, PhD.
Faculty of Electrical Engineering, Computer Science and Information Technology Osijek
JOSIP JURAJ STROSSMAYER UNIVERSITY OF OSIJEK
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Workshop – day 3:

## Slide 2: Content
Workshop in 3 parts
Materials on: https://loomen.carnet.hr/course/view.php?id=11343#section-5
PART 1 (9:30-11:30 h):
  About mathematical notation of optimization problem
  Short overview of optimization methods
  Metaheuristic, bio-inspired optimization techniques
  Overview of optimization problems in distribution power networks
  Overview of optimization and simulation tools (open source tools accented)
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 3: Content
PART 2 (12:00-13:30 h): :
  Examples of analytically given optimization problem in PYTHON (including exercises on PC)
  Introduction in OpenDSS simulation tool
  Generating OpenDSS scripts for distribution power network examples (including exercises on PC)
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 4: Content
PART 3 (13:45-15:30 h): :
  Brief description of co-simulation setup through interfacing OpenDSS and PYTHON optimization tool
  Examples of optimizations in distribution power networks by using co-simulation setup (including exercises on PC)
  Presentation of multiobjective optimization
  Examples of multiobjective optimizations in distribution power networks by using co-simulation setup (including exercises on PC)
  Overview of used sources and sources for further self-improvement.
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 5: PART 1: about optimization
Mathematical description (single objective)
Objective function (OF)
Vector of decision variables (DV)
Constraints:
Equality
In-equality
Box (Bounds)
T e.g. one DV
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 6: PART 1: about optimization
Schematic presentation
Optimization Problem (OP)
Decision variables
OF input
OF values
OF output
OF and constraint calculations
Optimizer (solver)
Until min OF is obtained
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 7: PART 1: about optimization
Features of the optimization problem parts (application in engineering)
Objective function (OF) and constraints:
Mathematical model of the real engineering system
Based on physical properties of the system or based on experimental data (T e.g. U-I char., Ohm law)
Both models can be analytical or numerical
Physical model: analytical (equation in closed form), numerical (equation is solved by numerical (iterative) method)
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 8: PART 1: about optimization
Features of the optimization problem parts (application in engineering)
Experimental model: analytical (aproximation of measured dana by function using curve fitting approach), numerical (raw measured data set)
Based on model properties OF and constraints can be:
  Continuous or discontinuous
  Differentiable or non-differentiable
Objective function (OF) and constraints:
Based on model properties DV can be:
  Real or discrete (integer)
Decision variables (DV):
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 9: PART 1: about optimization
Optimization techniques – main classification, requirements on OP
Conventional (classic): works with analytically expressed objective function
Metaheuristic (heuristic): works with numerical values of the objective function
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 10: PART 1: about optimization
Optimization techniques – main classification, requirements on OP
Optimization/OP properties | Conventional (classic) | Metaheuristic
Objective, Constraints | continuous, differentiable (smooth) | continuous, discontinuous, differentiable, non-differentiable
Decision variables | real, integer(some methods) | real, integer(some methods), linguistic
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 11: PART 1: about optimization
Metaheuristic optimizations
Features (advantages):
  Population based (parallel search in the solution space)-avoiding stuck in local optimums
  Easy to implement in a programing environment-a number of existing solutions in different programing languages
  Have no any requirements on objective functions and constraints form-makes them appropriate for “black box” optimization
Nature-inspired mostly
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 12: PART 1: about optimization
Metaheuristic optimizations
Features (drawbacks):
  Large number of objective (and constraints) calculations-high computational effort, possible high computational time (time expensive objective)
  No guaranties to achieve global optimum-near to global optimum solvers
  Convergence speed and solution quality depends on solver internal parameters-need for solver parameters tuning (mostly by experiments)
Nature-inspired mostly
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 13: PART 1: about optimization
Metaheuristic optimizations
Nature-inspired optimization methods:
  Bio-inspired
    Evolutionary Algorithms (EAs)
    Swarm based, Swarm Intelligence (SI)
  Physical-inspired
  Chemical-inspired
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 14: PART 1: about optimization
Evolutionary Algorithms
EAs:
  Mimic (very simple form) the evolution process in the nature
  Drive population of solution through iterative process to the problem solution
  Optimization solver is based on evolutionary operators: crossover, mutation and selection
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 15: PART 1: about optimization
General scheme of EA
Initial population of solutions
Objective (fitness) function calculation
Parents selection
Crossover to generate offspring (recombination)
Offspring mutation
Generate new population (selection)
Until the stopping criteria is satisfied
Evolutionary Algorithms
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 16: PART 1: about optimization
Evolutionary Algorithms
Environmental adaptation, main quality
Individual’s gene consists of chromosomes
Environmental adaptation, decrease or annul main individual’s quality (ability)
Nature’s equivalent
Optimization Problem
Environment, Habitat
Math model
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 17: PART 1: about optimization
Evolutionary Algorithms
Main type of EAs:
  Genetic Algorithms (GA)
  Evolutionary Strategy (ES)
  Differential Evolution (DE)
  Genetic Programming (GP)
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 18: PART 1: about optimization
Optimization problems in distribution electric power network
Some examples:
  Allocation of devices
  System and devices control
  Optimal Power Flow
  Parameters identification
  System and device design
  Network configuration
  …
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 19: PART 1: about optimization
Optimization problems in distribution electric power network
  Devices allocation
  Where
  and what size?
  Objectives:
  Power losses
  Flatness of feeder voltage profile
  Voltage drop
  Financial benefit
  Solution:
  DG locations
  DG sizes
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 20: PART 1: about optimization
Optimization problems in distribution electric power network
  Control
  PDG, QDG?
  Objectives:
  Power losses
  Flatness of feeder voltage profile
  Voltage drop
  Financial benefit
  Solution:
  DG power injections over the time
  DG allocation
Chart: MIN Losses
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 15 | 15 | 16 | 16 | 17 | 17 | 18 | 18 | 19 | 19 | 20 | 20 | 21 | 21 | 22 | 22 | 23 | 23 | 24
P DG1 | 357.2401 | 357.2401 | 364.3756 | 364.3756 | 296.3165 | 296.3165 | 362.7213 | 362.7213 | 343.1306 | 343.1306 | 371.9262 | 371.9262 | 379.0361 | 379.0361 | 269.058 | 269.058 | 336.6768 | 336.6768 | 380.8933 | 380.8933 | 347.4186 | 347.4186 | 352.8544 | 352.8544 | 406.8622 | 406.8622 | 283.2093 | 283.2093 | 426.879 | 426.879 | 430.9644 | 430.9644 | 430.2501 | 430.2501 | 414.8422 | 414.8422 | 378.9225 | 378.9225 | 387.0877 | 387.0877 | 400.1918 | 400.1918 | 357.8517 | 357.8517 | 417.1397 | 417.1397 | 505.2843 | 505.2843
Q DG1 | -114.1471 | -114.1471 | -22.4236 | -22.4236 | 58.4633 | 58.4633 | -150.8454 | -150.8454 | -2.7166 | -2.7166 | 22.8457 | 22.8457 | 30.8652 | 30.8652 | 118.2754 | 118.2754 | 93.9468 | 93.9468 | 55.4211 | 55.4211 | 157.3945 | 157.3945 | 15.6308 | 15.6308 | 48.2595 | 48.2595 | 96.2032 | 96.2032 | 81.6594 | 81.6594 | 126.258 | 126.258 | 84.4794 | 84.4794 | 90.6183 | 90.6183 | 97.6477 | 97.6477 | 90.607 | 90.607 | 74.4422 | 74.4422 | 57.2835 | 57.2835 | 0.36361 | 0.36361 | 118.9665 | 118.9665
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 21: PART 1: about optimization
Optimization problems in distribution electric power network
  Parameters identification
  Ri, Xi?
  Objectives:
  Difference between measured and calculated quantities
  Solution:
  Ri, Xi
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 22: PART 1: about optimization
Power system simulation and metaheuristic optimization tools
Source: https://wiki.openelectrical.org/index.php?title=Power_Systems_Analysis_Software
39 – commercial 27 – Free (Open source)
Power flow, short circuit, OPF
Transient analysis
…
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 23: PART 1: about optimization
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
  Commercial:
    modeFRONTIER
    MATLAB (toolbox)
    Mathematica
    …
  Free (Open source):
    HeuristicLab
    jMetal
    Pyevolve
    DEAP
    PyGMO
    …
Power system simulation and metaheuristic optimization tools
Research at: https://en.wikipedia.org/wiki/List_of_optimization_software

## Slide 24: PART 1: about optimization
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Workshop working simulation tools
  OpenDSS, simulation of distribution network systems
http://smartgrid.epri.com/SimulationTool.aspx
  Python Scientific Computing Package
https://www.scipy.org/

## Slide 25: PART 1: about optimization
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Using SciPy metaheuristic optimization (DE)
  Genetic operators in DE:
    Mutation
    Crossover
    Selection
  DE parameters: F – mutation factor, Cr – crossover rate

## Slide 26: PART 1: about optimization
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Using SciPy metaheuristic optimization (DE)
scipy.optimize.differential_evolution (OF, DEpar1, DEpar2, …)
Py function calculating objective function value
def OF (ind, *addPar):
some code …
Box constraints of optimization problem

## Slide 27: PART 1: about optimization
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Using SciPy metaheuristic optimization (DE)
Explanation on: https://docs.scipy.org/doc/scipy-0.17.0/reference/generated/scipy.optimize.differential_evolution.html
  SciPy DE:
  scipy.optimize.differential_evolution(OF, Box cnstr., maxiter=100, popsize=15, mutation=(0.5, 1), recombination=0.7, disp=True, polish=False)
  F – mutation factor, Cr – crossover rate

## Slide 28: PART 1: about optimization
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Additional sources for self-study and further research
Optimization problem definition:
  J. Hedengren, “Design Optimization Textbook.” [Online]. Available: http://apmonitor.com/me575/index.php/Main/BookChapters
Metaheuristic optimization overview:
  S. Bandaru and K. Deb, “Metaheuristic Techniques.”, https://pdfs.semanticscholar.org/c28f/cda2bccc75b10e1d540031269e82a5d9c9b0.pdf?_ga=2.130438726.859446823.1553504960-1592470437.1516282346
  S. Binitha and S. Siva Sathya, “A Survey of Bio inspired Optimization Algorithms 138,” Int. J. Soft Comput. Eng. , vol. 2, no. 2, pp. 137–151, 2012.
  I. Fister, X.-S. Yang, I. Fister, J. Brest, and D. Fister, “A Brief Review of Nature-Inspired Algorithms for Optimization,” Elektroteh. Vestn., vol. 80, no. 3, pp. 1–7, 2013.

## Slide 29: PART 1: about optimization
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Additional sources for self-study and further research
Evolutionary algorithms:
  A. E. Eiben and J. E. Smith, Introduction to Evolutionary Computing. Berlin, Heidelberg: Springer Berlin Heidelberg
Metaheuristic optimization in power system:
  M. Gavrilas, “Heuristic and metaheuristic optimization techniques with application to power systems,” in Proceedings of the 12th WSEAS international conference on Mathematical methods and computational techniques in electrical engineering, 2010, pp. 95–103.
  J. Radosavljevic, Metaheuristic Optimization in Power Engineering. Institution of Engineering and Technology, 2018

## Slide 30: PART 1: about optimization
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Coffee break – 30 min