## Slide 1: Theory and implementation of optimisation methods for optimizations in distribution power system – PART 3
Marinko Barukčić, PhD.
Faculty of Electrical Engineering, Computer Science and Information Technology Osijek
JOSIP JURAJ STROSSMAYER UNIVERSITY OF OSIJEK
Workshop – day 3:
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek

## Slide 2: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Network simulation – optimization tools co-working

## Slide 3: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Network simulation – optimization tools co-working
  Python – OpenDSS co-simulation setup
  Through COM interface or OpenDSSDirect.py
  Access to OpenDSS COM:
  import win32com.client
  dssObj = win32com.client.Dispatch(“OpenDSSEngine.DSS”)

## Slide 4: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Network simulation – optimization tools co-working
  Python – OpenDSS co-simulation setup
  Interfaces to COM:
  dssText = dssObj.Text # intfc. to text editing in script
  dssCircuit = dssObj.ActiveCircuit # intfc. to circuit model
  dssSolution = dssCircuit.Solution # intfc. to solution method
  dssElem = dssCircuit.ActiveCktElement # intfc. to model element

## Slide 5: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Network simulation – optimization tools co-working
  Python – OpenDSS co-simulation setup
  Compile OpenDSS file:
  dssText.Command = r"Compile 'E:\Google_Drive_on_E\ZNANSTVENO-PhD\ZNANSTVENO\POSTDIPLOMSKI\ZNANST-RADOVI\2017\ELMAkonf-Sofija-Bulgaria\PYTHON\IEEE13estLOAD.dss'"
  Path to the script
  OpenDSS filename (script you made before)

## Slide 6: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Network simulation – optimization tools co-working
  Python – OpenDSS co-simulation setup
  Access to model element and change par. value:
  dssCircuit.Loads.Name = L1 # set load L1 as active load
  pf0 = dssCircuit.Loads.pf # get load power factor value of L1
  dssCircuit.Loads.pf= 0.9*pf0 # set new pf value of L1

## Slide 7: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Network simulation – optimization tools co-working
  Python – OpenDSS co-simulation setup
  Done simulation and get results:
  dssSolution.Solve() # execute simulation
  loss = dssCircuit.Losses
  Stot = dssCircuit.TotalPower
  Vph = dssCircuit.AllBusVolts
  Vpu = dssCircuit.AllBusVmagPU
  …
  https://sourceforge.net/p/electricdss/code/HEAD/tree/trunk/Distrib/Doc/OpenDSS%20Circuit%20Interface.pdf

## Slide 8: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
  ‘black box’ optimization – OF value is obtained through simulation
  Exercise 3:
  Find optimal allocation (size and position) of DG unit in distribution network with aim to obtain minimum active losses in the network.
Network simulation – optimization tools co-working

## Slide 9: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
  ‘black box’ optimization – problem overview
  Exercise 3:
  Where
  and what size?
Network simulation – optimization tools co-working

## Slide 10: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
  ‘black box’ optimization – optimization scheme
  Exercise 3:
Initial population of solutions
PYTHON (DE)
Objective (fitness) function calculation
OpenDSS
Parents selection
PYTHON (DE)
Crossover to generate offspring (recombination)
PYTHON (DE)
Offspring mutation
PYTHON (DE)
Generate new population (selection)
PYTHON (DE)
Until the stopping criteria is satisfied
Network simulation – optimization tools co-working

## Slide 11
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
  Exercise 3:
  Task in OpenDSS script:
    New Generator.DG1 bus1=LOCd … (Add DG)
  Specific tasks –PY script:
    Set COM interface to OpenDSS
    Coding decision variables as DE individual
    Add DG unit to prepared OpenDSS script directly in OpenDSS script
Network simulation – optimization tools co-working
PART 3: co-simulation

## Slide 12: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
  Exercise 3:
  Specific tasks – PY script:
    Formulate the optimization problem in black-box approach – function in Python including interface to OpenDSS
    Formulate and code constraints – simultaneously with coding the objective function
    Defining ranges (limits) of the decision variables
    Execute optimization and show results
Network simulation – optimization tools co-working

## Slide 13: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
  Exercise 3:
  Decision variables coding (T expl.)
    DV = [DGL, DGP, DGQ] location is discrete but DE works with real numbers !?!
  Constraints (T expl.)
    Voltage constraints
    DG production constraint
  Objective function
    Calculate OF value by using simulation tool
Network simulation – optimization tools co-working

## Slide 14: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Network simulation – optimization tools co-working
  Exercise 3:
  Code locations: LOC = [bus 1, bus2, … busN]
  DGL = round(ind[0])
  Decode locations LOCd = LOC[DGL]
  Box constraints
    DV ranges: DVL = [(0, len(LOC)), (Pl, Pu), (Ql, Qu)]

## Slide 15: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Network simulation – optimization tools co-working
  Exercise 3:
  Change location , active and reactive power of DG from Python:
  dssText.Command = 'Edit generator.DG1' + ‘bus1=‘ + LOCd + ' kw=‘ + str(ind[1]) + ' Kvar=‘ + str(ind[2])

## Slide 16: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
Subject to: solution:

## Slide 17: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Pareto set and Pareto front
  Not one solution but solution set!!
  Decision maker has possibility to choose the currently most appropriate solution.

## Slide 18: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Pareto dominance definition
  The best (optimal) solution is non-dominated solution.
  Two non-dominated solutions are same quality.

## Slide 19: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Pareto ranking method

## Slide 20: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Python tool for MOOP solving
  Distributed Evolutionary Algoritms in Python - DEAP
  https://deap.readthedocs.io/en/master/
  Flexible tool with possibilities for building custume EA combining different versions of EA elements (operators, individual coding, sorting…)

## Slide 21: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  MOOP – optimal allocation of DG in distribution network
  Exercise 4 (T expl.):
  Where
  and what size?
  Two objective functions, f1 - total active looses and f2 – active DG power, both minimization

## Slide 22: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Specific tasks (T expl.):
    Set COM interface to OpenDSS
    Coding decision variables as DEAP EA individual
    Add DG unit to prepared OpenDSS script directly in the script
    Formulate the optimization problem in black-box approach – function in Python including interface to OpenDSS

## Slide 23: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Specific tasks (T expl.):
    Formulate and code constraints – simultaneously with coding the objective function
    Defining ranges (limits) of the decision variables
    Execute optimization by using DEAP and show results

## Slide 24: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Solution:
    Add DG unit in OpenDSS script prepared in Exercise 2:
    New Generator.DG1 bus1=LOCd …
    Change location and power of the DG by EA:
    LOCd = LOC[DGL]
    dssText.Command = 'Edit generator.DG1' + ‘bus1='+LOCd+' kw='+str(ind[1])+' Kvar='+str(ind[2])

## Slide 25: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Solution:
    DEAP module initiation:
    import deap
    from deap import algorithms, base, creator, tools
    Set fittnes and individual types:
    creator.create("FitnessMin", base.Fitness, weights=(-1.0,-1.0))
    creator.create("Individual", list, fitness= creator.FitnessMin)

## Slide 26: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Solution:
    Instantiate DEAP toolbox class:
    toolbox = base.Toolbox()
    Registration of decision variable form, individual and population types
    toolbox.register("dv1", random.randint, L1, U1)
    toolbox.register("ind", tools.initCycle, creator.Individual, (toolbox.Nl, toolbox.Nn), n=1)
    toolbox.register("population", tools.initRepeat, list, toolbox.ind)

## Slide 27: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Solution:
    Generating initial population:
    pop = toolbox.population(n=nP)
    Registration of EA operators crossover, mutation and selection
    toolbox.register("mate", tools.cxUniform, indpb = 0.5)
    toolbox.register("mutate", tools.mutPolynomialBounded, low=[L1, L2], up=[U1, U2], eta=20.0, indpb=0.05)
    toolbox.register("select", tools.selNSGA2)

## Slide 28: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
Multiobjective optimization problem – MOOP
  Solution:
    Registration of the objective function:
    toolbox.register("evaluate", OF)
    Optimization starting
    res, log = algorithms.eaMuPlusLambda(pop, toolbox, mu=toolbox.pop_size, lam=toolbox.pop_size, cxpb=1-toolbox.mut_prob, mutpb=toolbox.mut_prob, stats=None, ngen=nG, verbose=True)
    Get solution as Python variable
    DVsol = np.array(res)

## Slide 29: PART 3: co-simulation
Faculty of Electrical Engineering, Computer Science and
Information Technology Osijek, April 2019, Osijek
THE END
Wish success with further implementation of optimization.